## Slide 1
II.2 Further harmonisation needed: gas day, nominations…
September 23, 2013

## Slide 2
The final purpose of the capacity bought by Network Users is to be used (nominated) by them. Therefore, when daily and with-day auctions will be implemented, nomination and renomination processes have to be accordingly adapted.
Nevertheless, this adaptation not only means to introduce additional renomination cycles but also harmonisation of gas day period, combustion reference temperature and automatic data exchange.
1. Background
To buy
capacity
To use capacity
Renomination
cycles
Gas day period
Combustion reference temperature
Automatic data exchange
September 23, 2013

## Slide 3
2. Gas Day Period
September 23, 2013
Historically adjacent countries have established different gas day periods. Therefore, TSOs and Network Users have dealed with this situation during the nomination/renomination and matching process.
If additional renomination cycles are implemented, the renomination deadlines are frequently established with reference to the gas day period. Consequently, if the gas day period is different in each border of the IP, then renomination deadlines will be different as well.
Gas day period from 5 to 5 UTC
First renomination cycle starts with the starting of the gas day
First renomination cycle=5 UTC
Gas day period from 23 to 23 UTC
First renomination cycle starts with the starting of the gas day
First renomination cycle=23 UTC
According to this example, no matching process can be performed until the first common renomination deadline. Therefore, until 5 UTC, renomination cycles of country B are useless because no nomination in country A has been sent yet.
Gas day period harmonisation is neccesary in order to get a successful additional renomination cycles implementation.
COUNTRY A
COUNTRY B

## Slide 4
3. Combustion Reference Temperature
Traditionally adjacent countries have established different combustion reference temperatures. Consequently, TSOs and Network Users have dealed with different problems during the nomination and matching process.
At each side of the IP, nominations and are sending by network users according to the combustion reference temperature in place. Nevertheless, for matching purposes, TSOs have to agree on one common combustion reference temperature and for this reason conversions factors have to be applied.
If additional renomination cycles are implemented the use of conversion factor will be strongly increased.
Network
User X
Nomination=5
(Tref=25ºC)
Nomination=5,013
(Tref=0ºC)
TSO A
TSO B
Nomination = 5
(Tref=25ºC)
Results of matching = 5
(Tref=25ºC)
Network
User X
Nomination Confirmed=5
(Tref=25ºC)
Nomination Confirmed=5,013
(Tref=0ºC)
Because both TSOs and Network Users have to manage conversion factors the risk of mismathing is currently high. On the other hand, the use of conversion factors involves rounded processes that cause some errors and claims.
It is seemed to be clear that if additional renomination cycles are implemented these kind of problems are going to be increased.
Combustion reference temperature harmonisation is neccesary in order to get a successful additional renomination cycles implementation.
COUNTRY A
COUNTRY B
September 23, 2013

## Slide 5
4. Automatic Data Exchange
Initially nomination and matching information was exchanged between TSOs by email. Although this kind of solution was suitable in the past, if additional renomination cycles are implemented it is a must to exchange this information automatically in order to:
Avoid mistakes: Excel files could contain transcription mistakes.
Comply with deadlines: The data volume to be exchanged each renomination cycle require automatic data exchange solutions
Guarantee information security: Whereas emails could contain mistakes in senders and recipients, automatic data exchange solution might include security measures to prevent unauthorised information access.
September 23, 2013

## Slide 6
4. Current Harmonisation Status
September 23, 2013

## Slide 7
September 23, 2013
Thank you for your attention!!!