## Slide 1
Amine Abada
06/10/2014
ERI SWE
TERRE #2
Trans European Replacement Reserve Exchange

## Slide 2
Please take in consideration these slides as the study state of the TERRE project
The information provided is under improvement and do not reflect the final stage of the project

## Slide 3
Offers

## Slide 4
Definition of standard products
Updated proposal - Introduction
TERRE Product  in line as close as possible with the RR standard product definition (current draft). The TERRE platform must treat the Standard products from its implementation (beginning)
Compliant with TSOs requirements
Delivery Period should be included in 1h time window
TERRE product  Scheduled product/Manual activated
15min < Full Activation Time(FAT) < 30min
TSOs have the possibility to convert local balancing product into TERRE Standard product

## Slide 5
Structure of standard balancing product
1- Preparation period = NA
2- Ramping period = NA
3- Min quantity = 1 MW
4- Delivery period = 15 min, 30min, 45min or 60min (depends on divisibility)
5- Deactivation period = Ramping period
Basic criteria
Time Divisibility : 15min or 30min
Definition of standard products
Updated proposal
2b- Full activation time = Between 15 min and 30min
2b
4
5
3
Quantity divisibility: 1MW
BRPs can propose an offer which represents several products
The matching algorithm will select the offer and “use” the product needed
3- Max Delivery period = 60 min

## Slide 6
Definition of standard products
Updated proposal - Characteristics
4
3
Energy volume considered in the matching process
The others characteristics must be defined in order to be taken into account by the solution:
The price
When the offer should be activated in order to be matched with TSO(s) need(s)
The TERRE solution must be compliant with the target of NC EB
Processing of standard products
Optimization algorithmic compliancy, results and activations…
=

## Slide 7
Definition of standard products
Linked offers / firmness of offers
In fact, the offers could be linked with others
Ex: the BRP can give the information that if we call for product 1 (Delivery period 15min) the TSOs (the TERRE solution) must activate product 2 (Delivery period 30min)
This “new” parameter must be considered by the TERRE solution
Remark: for TERRE, the offers could be linked but within the same CMO (CMO RR)
Once the offer is selected by the matching process and asked for activation, the TSO which submitted the offer is responsible (also financially) for its delivery on its border.

## Slide 8
Needs and matching

## Slide 9
TERRE process
TERRE
XB
Capacity
TSOs
Products
Needs
Needs netted and matched
Offers which must be activated
TSOs
XB capacity used
??

## Slide 10
Needs
Each TSO must submit to TERRE, after the ID GCT and before the TERRE algorithmic matching process, the need expected for the next hour/delivery period
The methodology for needs determination is under the responsibility of each the TSO
We present in the next slides, how the needs could be matched with other (opposite) needs or products

## Slide 11
Matching process
The project focus its studies on algorithmic matching
After the qualitative study and first prototype (simplistic) which concluded that for TERRE the must efficient solution is an algorithmic optimization based on implicit auctions model, the project will make a second study presenting “mathematical equations”
The project will process quantitative simulations in order to demonstrate that this solution could be implemented at a “industrial” level

## Slide 12
Structure of TSO need (example)
Definition of standard products
Possible approach for matching of needs
= XB scheduling step = 1h
H
H+1h
H-1h
Matched by XB or local products
Matched only by local products ?
The TSO (Control Block) net position ( ) updated by TERRE results must be the same fore the whole delivery hour  LFC process
Delivery period
ID Market
TERRE processing
Matched by or local products
XB scheduling step = 30min